## Slide 1
Declared Distances

## Slide 2: Why do we need Declared Distances data?
“The accelerate-stop distance must not exceed the length of the runway plus the length of any stopway.”,
“The takeoff distance must not exceed the length of the runway plus the length of any clearway except that the length of any clearway included must not be greater than one-half the length of the runway.”
“The takeoff run must not be greater than the length of the runway.”
Operating Rules – 14 CFR 91, 121, or 135

## Slide 3: Aeronautical Information Manual (AIM) Use of Runways/Declared Distances

## Slide 5: Declared Distances
The distances declared available for an aircraft’s takeoff run, takeoff distance, accelerate-stop distance, and landing distance requirements.
Notes: While a runway may have a defined length, the entire length may not be available for takeoff or landing.
Alternatively, extra length may be available for specific operations.

## Slide 6: Declared Distances
  Takeoff Runway Available (TORA)
  Takeoff Distance Available (TODA)
  Accelerate Stop Distance Available (ASDA)
TAKEOFF OPERATIONS
ARRIVAL OPERATIONS
Start of TORA, TODA, & ASDA
Start of LDA
Start of LDA
Consists of:
  Landing Distance Available (LDA)
Notes: TORA/TODA/ASDA - The start of the takeoff will always be collocated. Typically the start of takeoff is at the beginning of the runway. Displaced thresholds do not effect the start of TORA, TODA, and ASDA.
LDA - The start of the LDA is at the beginning of the runway, unless the threshold is displaced.

## Slide 7: TakeOff Run Available (TORA)
The runway length declared available for the ground run of the airplane.
  TORA does not exceed the length of the runway
  TORA does not exceed the length of the TODA
Takeoff Run Available (TORA)
Notes: Takeoff Run Available is the runway length declared available for the ground run of the airplane.
Emphasize “ground run”.
Typically the TORA will equal the runway length.
The TORA is not to exceed the length of the runway, and must not exceed the length of the Takeoff Distance Available (TODA).

## Slide 8: TakeOff Distance Available (TODA)
The length of the Takeoff Run plus the length of the clearway, if provided.
TODA = TORA + Clearway
Takeoff Distance Available (TODA) – normal case
Clearway Plane
Takeoff Distance Available (TODA) – with clearway
Notes: TODA is the length of the Takeoff Run plus the length of the clearway, if provided.
Clearways are areas not suitable for stopping the airplane in the event of an aborted take-off, but adequate to provide additional take-off distance for climb-out.
It is expected the aircrafts wheels will be off the ground once it reaches the clearway.
Clearways are not very common, therefore TODA typically equals the TORA length.

## Slide 9: Clearway (Title 14 §1.1)
STANDARDS
Width = At least 500 feet
Length = No more than half the runway
Slope: 80:1 (1.25%)
Clearing: No object, except for threshold lights no higher than 26 inches and located on the sides of the runway.
Control: Airport owner control
Notes: Clearway is an area beyond the end of the runway that may be used as part of the takeoff distance calculation. For certain operations, a clearway can be used in lieu of actual runway to satisfy takeoff distance requirements.
Example: A pilot is departing a 5,000 foot long runway with a 500 foot clearway. When determining takeoff distance, the pilot can add the extra 500 foot clearway in their calculation. In other words, they can consider their takeoff distance available as 5,500 feet, and not just the 5,000 paved runway.
Clearways are not common and not many exist today in the NAS.
  Because the runways we build typically provide adequate runway length w/o needing a clearway.
  Clearway standards as defined in 14 CFR Part 1 is very stringent and challenging for many airports to conform to.
In order to be used as part of the takeoff distance, the clearway must meet legally defined criteria. MOS not allowed!
Width The clearway must be at least 500 feet wide symmetrically about the runway centerline.
Length The length is no more than half the runway length.
Slope The clearway plane slopes upward with a slope not greater than 1.25 percent (80:1).
Clearing No object or terrain may protrude through the clearway plane except for threshold lights no higher than 26 inches and located off the runway sides. The area over which the clearway lies need not be suitable for stopping aircraft in the event of an aborted takeoff.
Control A condition for clearways is that the airport owner have suitable control of the underlying property. Direct ownership is not necessary, however ownership offers the highest degree of control. The purpose of such control is to ensure that no object penetrates the clearway plane during a takeoff operation.

## Slide 10: Accelerate Stop Distance Available (ASDA)
The length of the Takeoff Run plus the length of the stopway, if provided.
ASDA = TORA + STOPWAY
Accelerate Stop Distance = TORA (normal case)
Stopway
Accelerate Stop Distance – with stopway
Notes: ASDA is the total distance available for an aircraft to accelerate to a specified speed and, assuming failure of an engine at the instant that speed is attained, to bring the airplane safely to a stop on the remaining runway. AKA aborted takeoff.
The ASDA distance is typically equal to the TORA. In the unlikely event a stopway is provided, the ASDA distance increases by the length of the stopway.
Stopways are essentially extra room used for the deceleration of an airplane aborting a takeoff.

## Slide 11: Stopway (Title 14 §1.1)
STANDARDS
Width: At least as wide as the runway.
Surface Strength: Able to support an aircraft during an aborted takeoff without causing structural damage to the aircraft. Refer to AC 150/5320-6 for pavement design standards for a stopway.
Notes: Stopways is defined in Title 14, Part 1 and has its own set of requirements. MOS is not allowed!
Stopways are not blast pads.
Stopways are used to decelerate an aircraft.
Blast pads are intended for erosion control from jetblast.
The presence of a blast pad does not mean a stopway exists. Stopways must be reported and reflected in the publication of Declared Distances.
Stopways are not common, primarily because they cannot be used as a RSA. And stopways are less cost effective in comparison to a full-strength runway that is functioning in both directions.
https://www.faa.gov/airports/airport_safety/certalerts/media/cert0003.pdf

## Slide 12: Landing Distance Available (LDA)
The length available and suitable for landing an airplane
Landing Distance – with displaced threshold
Landing Distance – normal case
Notes: Typically the landing distance is equal to the runway length.
When the threshold is displaced, the LDA is the runway length minus the displacement.

## Slide 13: Declared Distances Summary

## Slide 14: PUBLICATIONS

## Slide 15: Chart Supplement, AMR, NOTAM
Notes: Left Side: Chart Supplement for Ronald Regan Airport, with its published declared distances. Declared Distances are published for each operational end. For Ronald Regan Airport, six published declared distances for each direction of their three runways.
Right Side: Excerpt from the FAA NOTAM Order discussing D.D.

## Slide 16: Airport Diagrams & Instrument Approach Charts
Notes: FAA publications use a “D” symbol is used to inform operators that there are declared distances established for one or more runways for this airport.
Pilots should then refer to the Chart Supplement or other publication to obtain these distances.
*************************************************
Jeppeson is a little different as they publish usable lengths distances and not declared distances, as they have been using this terminology before the creation of declared distances.

## Slide 17: CertAlert No. 09-05
https://www.faa.gov/airports/airport_safety/certalerts/
Notes: Published in 2009, AAS-300 issued a Cert Alert requiring all runways available for air carrier use to have its declared distances reported.

## Slide 18: Runways without Published Declared Distances
Assumed to be equal to the physical length of the runway.
Notes: For runways without published declared distances, the declared distances may be assumed to be equal to the physical length of the runway unless there is a displaced landing threshold, in which case the Landing Distance Available (LDA) is shortened by the amount of the threshold displacement.

## Slide 19: Visual Cues of Declared Distances
Notes: No visual cues regarding declared distances with a few exceptions.
  Exception #1 – Runways with a displaced threshold is a visual indicator that the LDA is shortened.
  Exception #2 – Airfield Information signs providing takeoff runway available information. Shown on the screen is one for temporary construction.

## Slide 20: Policy Guidance Memo
https://www.faa.gov/airports/engineering/media
Notes: AAS and APP joint memo on DD for non-turbine powered airplanes.

## Slide 21: Declared Distances and Airport Design

## Slide 22: Considerations
TORA | Departure RPZ
TODA | Clearway Departure Surface
ASDA | Stopway Runway Safety Area Runway Object Free Area
LDA | Runway Safety Area Runway Object Free Area Approach Surface Approach RPZ

## Slide 23: Takeoff Runway Available (TORA)
The runway length declared available for the ground run of the airplane.
Departure RPZ
TORA
NOT TO SCALE
9
200’

## Slide 24: Shortening TORA
TORA
TORA
RUNWAY PROTECTION ZONE
Incompatible Land Use
RUNWAY PROTECTION ZONE
NOT TO SCALE
Incompatible Land Use
AC 150/5300-13B: FAA does not recommend reducing the TORA on runways to mitigate incompatible land uses in the departure RPZ.
9
9
Notes: Safety Risk Panel with both internal and external subject matter experts to identify hazards associated with the current practice of reducing the TORA to satisfy the departure RPZ.
No hazards were found, however a finding that the TORA reduction to mitigate the departure RPZ may not achieve the safety benefit as intended.
Departure RPZ is applicable to all aircraft, but declared distances is not.
Previous MITRE study identified Part 23 aircraft and Part 91 operations have a considerably higher risk versus Part 25 and 121/135 operators. So if we are reducing the TORA to satisfy the departure RPZ, the aircraft of higher risk can legally ignore the reduced TORA distance. The aircraft of low risk (Part 25 aircraft operating under 121 or 135) are impacted and in some situations required to decrease takeoff weight to satisfy the reduced TORA.

## Slide 25: Takeoff Distance Available (TODA)
The length of the Takeoff Run plus the length of the clearway, if provided.
40:1 Departure Surface
Clearway
NOT TO SCALE
9
TODA = TORA + Clearway
Notes: The TODA considers both the clearway and the departure surface. In the unlikely event a clearway is provided, the TODA will be the TORA plus the length of the clearway.

## Slide 26: Shortening TODA
40:1
NOT TO SCALE
END OF TODA
END OF TORA
Notes: TODA can be shortened to meet the 40:1 departure surface.
Note: shortening the TODA, also shortens the TORA as the TORA can never exceed the length of the TODA.
Shortening the TODA to meet the departure surface is just one method of mitigating penetrations to the departure surface. Other mitigations is handled by Flight Procedures in accordance with TERPS policy which may be the optimum mitigation.
Prior to reducing the TODA to satisfy the 40:1, it is recommended to coordinate with AFS and FP.

## Slide 27: Accelerate Stop Distance Available (ASDA)
The length of the Takeoff Run plus the length of the stopway, if provided.
NOT TO SCALE
Accelerate Stop Distance = TORA (normal case)
Stopway
Accelerate Stop Distance – with stopway
9
RSA
ROFA
RSA/ROFA Length

## Slide 28
ASDA
STOPWAY
ASDA
ASDA
NOT TO SCALE
TYPICAL ASDA
ROFA
EXTENDED ASDA
ROFA
SHORTENED ASDA
RUNWAY
SAFETY AREA
RUNWAY
SAFETY
AREA
9
9
ROFA
9
RUNWAY
SAFETY AREA
Notes: Reducing the ASDA in this case shifts the RSA and ROFA footprint in a manner the roadway is no longer within its limit. To calculate the ASDA, you will need to determine how much you need to shift the RSA and ROFA to remove the roadway. You will then subtract that value from the standard RSA/ROFA length. Lastly, you take the Takeoff Run and subtract that final value to get your published ASDA. We will go through an example to better understand this.

## Slide 29: Landing Distance Available (LDA)
The length available and suitable for landing an airplane
LDA
NOT TO SCALE
9
Approach RPZ
Approach Surface
RSA
ROFA
Notes: Keep in mind for runway ends that are equipped with electronic or visual vertical guidance (such as a Glide Slope or PAPI), that the RSA length prior to the threshold may be shorter than the RSA length beyond the departure end. You will need to look at the Runway Design Code to determine if that would apply to the runway in question. For example, a C-III-2400 RDC has an RSA length of 600 feet prior to the threshold, not 1000 feet.

## Slide 30
ROFA
ROFA
ROFA
LDA
LDA
LDA
RUNWAY
SAFETY AREA
Displacement
Displacement
NOT TO SCALE
RUNWAY
SAFETY AREA
RUNWAY
SAFETY AREA
9
9
9
Notes: The first figure is your typical LDA, which is the distance from the threshold to the end of the runway. In this example, the RSA and ROFA are in full compliance.
The second figure shows a displaced threshold, so we know the LDA will not begin at the beginning of the runway but rather at the location of the threshold. The threshold may have been displaced due to an obstacle in the approach surface or incompatible land use within the approach RPZ.
One alternative to mitigate the RSA and ROFA is to reduce the LDA such that the roadway does not infringe upon the RSA and ROFA You will notice the LDA ends prior to the end of the runway to compensate for the roadway. This LDA will be the published length for arrivals.

## Slide 31: Example
Airport XYZ is looking to implement declared distances to satisfy the RSA standard for Runway 09/27. Provide the declared distances for this runway. Assume all other runway design standards are in compliance.
400 ft.
900 ft.
KNOWN
Runway Length = 5,000 ft.
RWY 9 Displacement = 500 ft.
RDC = C-III-2400
Both ends with ILS and GS
200 ft. Clearway
9

## Slide 32: Runway 9 Assessment
TORA = 5,000 feet
TODA = 5,000 + 200 (clearway) = 5,200 feet
ASDA = 5,000 – (1,000 – 900) = 4,900 feet
LDA = 5,000 – 500 - (1,000 – 900) = 4,400 feet
400 ft.
900 ft.
RWY 9 = 5,000 feet
500 ft.
9
LDA = 4,400’
TORA = 5,000’
TODA = 5,200’
ASDA = 4,900’
RSA = 1,000’
RSA = 1,000’

## Slide 33: Runway 27 Assessment
TORA = 5,000 feet
TODA = 5,000 feet
ASDA = 5,000 – (1,000 – 400) = 4,400 feet
LDA = 5,000 – (1,000 – 400) = 4,400 feet
400 ft.
900 ft.
RWY 27 = 5,000 feet
500 ft.
9
RSA = 1,000’
TORA = TODA = 5,000’
ASDA = LDA = 4,400’
Should the Runway 27 threshold be displaced to satisfy a RSA of 1,000 feet?

## Slide 34: Questions?